B1 Information Engineering Project
Calibrating a Digital Camera for Computer Vision

Introduction
Distances in an image or photograph can be measured somewhat accurately by defining and quantifying the camera. The aim of this project is to create a program that calibrates a fixed focus camera model and to assess the performance of the code.
The program first creates a camera model and builds a calibration grid image. The calibration grid image is then modified by adding noise and outliers, which represent anomalies in the algorithm that generates calibration grid measurements. The program attempts to use multiple calibration grid images to estimate the original camera model. Because the initial camera model is known, the accuracy of the estimated and optimised models can be compared with the original model.

Structure Overview
Any large coding project requires a structured approach, value checking, and proper commenting to be successful. This project was divided into four smaller, more managable steps: viewing an object with a camera model, estimating the homography, estimating the K-matrix, and optimising the K-matrix. The project was broken down further by writing a small piece of code and testing it with a harness script. For example, the first objective was to simulate a camera. This script was tested by plotting what a cube would look like viewed some angle and distance away, making it easy to verify the camera model.

Fig I. Output from viewCamera and using viewCamera code to view a tile calibration grid with noise and outliers

Because the code builds on itself in each step, testing the program after each new addition helps target bugs quickly instead of allowing a bug to go unnoticed and getting unexpected outputs in the future. In this case, code from viewing the cube with a camera was later used to view a calibration grid with both noise and outliers. By using a piecewise approach, testing whether each component was working as expected and building on preexisting work was straightforward.
 During the development process, the code was backed up and saved using a form of version control software called Github. Github allows users to push software changes to a repository along with version number and notes. The changes made are all tracked, making it easy to revert to an old program. Version control is an extremely important part of any large coding project. Projects are likely to have large teams tackling different aspects of the project at the same time. Team members can copy or ‘fork’ the main code to test new and experimental code and then merge changes together by combining branches of code.
Proper input and value checking statements in the code also ensured errors or inaccurate results were avoided. MATLAB’s calculation accuracy is limited because the minimum difference that its floating point arithmetic software can handle is given by eps, which has a value of approximately 2.22E-16. When normalising any values, a comparison between the denominator and eps was made. Checks to validate function inputs were also used, including matrix size and acceptable input value ranges.
Comments were also an important part of structuring the program. Comments were added to describe the structure, requirements, and limitations of the code. For example, when writing a new function, such as the computeImageErrors function, commenting was used to lay out the steps the function took in the header, making information about function readily accessible without opening the function file. In the code, comments described expected variable values and sizes. All newly initialised variables were also clearly defined and mathematical steps were explained throughout the code.

K-matrix Estimation
K-matrix Optimisation and Stopping Criterion
The optimisation function aims to minimize the variance from the back projection errors between the grid point correspondences. To achieve this, it uses the current best guess of the camera K-matrix to find the predicted positions of points in the camera image. It then finds the difference between the measured and predicted points and calculates the sum of the squared differences.
The Levenberg-Marquardt algorithm is used to optimise the K-matrix. The initial stopping criterion used was the norm of the gradient divided by the problem size (K-matrix components plus number of images times frame parameters). However, an improved stopping criterion is the infinity norm. The

Stopping Criterion

The stopping criterion used for the Levenberg-Marquardt theorem when the gradient is small is the norm of the gradient divided by the problem size. The gradient is

Because variables in the blocks have different units, it is important to scale *********************************** scale things
t

Writing code
Text

Error vector
The error between the predicted points and measured points were calculated by first building a 2n by 1 error vector containing the u point differences followed by the v points, where n is the total number of points. To find the error vector, two new matrices were built from Correspond points in the consensus set, one for the measured points and another for the predicted points. The predicted point locations in camera coordinates were found by using the axis-angle representation and the origin translation vector to build a rotation matrix relating grid coordinates to the camera frame. The rotation matrix was then used to transform the calibration grid coordinates into camera coordinates to obtain the predicted positions. The difference between the predicted and actual points were then subtracted and added to the error vector.

Calculating the Jacobian
The Jacobian is a matrix of the partial derivatives of a function. This program takes advantage of the fact that the change of parameters for one image does not affect the other images. Therefore, the Jacobian can be calculated individually for each image and the total Jacobian has a block structure. The function singleImageJacobian calculates two blocks, the K-matrix Jacobian and the Frame Jacobian. The single image K-matrix Jacobian is a 2n by 5 matrix, with each column representing the perturbation of an upper triangular k-matrix component, and the Frame Jacobian block is a 2n by 6 matrix of the partials from perturbing the rotational and translational vector components, where n is the number of points in the consensus set.
Partial derivatives were calculated by adding a proportional small change to the original value, calculating the resulting change in point positions, and then dividing the difference in position by the small step in parameter. The proportional small change was compared against eps to ensure accurate values. If the change was less than eps, the value was set at a small increment, which avoided numerical roundoff or division by zero.

K-matrix Accuracy & Code Limitations
The K-matrix estimation results were fairly accurate. On average, the K-matrix varied from the ________ for a random
Accuracy and performance time

Code Performance & Limitations
Code performance can be quantified by the accuracy of the resulting K-matrix and the amount of time and resources to solve for it.
To give a reasonable estimate of the program performance, the K-matrix was fixed to a random value within the allowed ranges and the number of RANSAC runs was increased. The number of RANSAC runs was then

Fig 2. Plots showing number of RANSAC runs versus Kmatrix error squared and function runtime. Dotted lines included for point clarity.

The largest amount of time running the program was spent on ransacHomog, originally accounting for approximately thirteen seconds of runtime out of a total of seventeen, as seen from the profile report below. This function uses norm to quantify the error between homogeneous points and corresponding points for each image, which is extremely costly.

Original ransacHomog profile report

This program estimates the K-matrix reasonably accurately in an acceptable amount of time.

Conclusion
This program reasonably estimates a camera model given six calibration images.
Further stages of development are required to achieve a fully functional product. The algorithm used to build the calibration grid has not been included in this program. For this business idea to be commercially viable, it would need to have an intuitive user interface. It may also benefit from being exported to another language or platform rather than MATLAB.
A potential GUI for this program would consist of some interface that allows the user to upload a number of calibration images as well as an image of an object. An end user could specify points of interest and the program could use the calculated matrix to find distances between the points.
While MATLAB is an ideal environment for writing and testing the code, the product could reach a larger audience if it were written in a more readily available platform. MATLAB is proprietary software that requires a license with a prohibitively high cost. Although MATLAB codes can be run by third-party services, such as the open-source Octave, the product would be much more streamlined if it could be run on a machine without the need to resort to either installing MATLAB or using an online service. Furthermore, MATLAB is an interpreted language, so the program is slower than if it were written with a compiled language. Using a compiled language could benefit the runtime and performance of this program since the program, once deployed, will most likely not need many changes.[1] The intellectual property in this product might also be easier to protect with a compiled language.
[1] Tranquillo, J. V. (2011). MATLAB for engineering and the life sciences. San Rafael, CA: Morgan & Claypool .